## Slide 1: S-112 Unit 12: Chainsaw Components, Maintenance, and Repairs
Notes: Tell students that during this unit, they will learn how to wear personal protective equipment (PPE) needed for chainsaw operations, identify chainsaw components, maintain a chainsaw, and start and stop a chainsaw.

## Slide 2: Objectives
Students will be able to:
Wear proper PPE.
Identify chainsaw components.
Perform chainsaw maintenance.
Perform a safety check.
Start and stop a chainsaw.
Notes: Review the unit’s objectives.

## Slide 3: Preparing To Use Your Chainsaw
What items should be part of your chainsaw kit?
Notes: Ask students to answer the following question: “What items should be part of your chainsaw kit?”
As students respond, take notes on flip chart paper or a whiteboard.
When debriefing, make sure that the following items are covered:
  PPE
  Chainsaw
  Felling Axe
  Wedges
  Sheath or scabbard (ideally, covers the guide bar, chain, dogs, and muffler)
  Chain file, filing guide, and raker file/depth gauge file (appropriate to the size of the chain being used as specified on the guide bar)
  Plumb bob
  Spare parts
  Scrench
  Filters
  Fuel
  Maintenance tools

## Slide 4: Chain Components
Identify and describe the different components of a saw chain.
Notes: Tell students that a saw chain comprises several parts that work together and must be adequately maintained for maximum performance and safety.
Ask students to volunteer to identify and describe different parts of the saw chain in the diagram (or on an actual chain on a chain saw) based on their prior experience.
When debriefing, make sure students correctly identify and describe the following components of their chainsaws:
  Drive link – fits in the bar groove so the bar can guide the chain around to the chain sprocket, allowing the power head to drive the chain. It also draws oil from the bar groove to lubricate the bar and chain. Explain that there is also a master link that joins both ends of the chain.
  Tie-strap – holds the chain together.
  Left-hand cutter – cuts the wood. The depth gauge (or raker) determines the depth of the cut.
  Right-hand cutter – cuts the wood. The depth gauge (or raker) determines the depth of the cut.
  Humped drive link – a low-kickback feature not found on all chains. Note that this should be in front of the cutter.
  Depth gauge (raker) - the depth gauge determines the height at which the cutter enters the wood and, thus, the thickness of the chip removed. The depth gauge setting is the difference between the top of the depth gauge and the top plate.

## Slide 5: Types of Chains
Chipper Chain
Chisel Chain
Semi-Chisel Chain
Notes: Tell students that the part of the chain called the cutter, also referred to as “teeth,” severs wood fibers. The saw chain has left-hand and right-hand cutters so that the saw chain will cut evenly through the wood.
Tell students this slide displays the three most common types of saw chain cutters (chipper, chisel, and semi-chisel). Ask students to identify the type of cutter on their chainsaws.
Tell students that it is common for units to only purchase one type of chain; however, they should be aware of the different types of chains available to them. Note that they would not, under most circumstances, change to a different type of chain in the field based on their assignment.
Explain what the different types of chains are used for:
  Chipper: The most versatile cutter type, the easiest to file, and tolerates dirt and dust. Cuts smoothly and is well-suited for most wildland fire chainsaw operations.
  Chisel: The most aggressive cutter type. Chisel comes in both round and square ground types.
    The round ground chisel requires the proper-size round file for proper sharpening. The square-ground chisel requires a double-bevel, hexagon, or single-bevel file to sharpen it.
    The square ground chisel is designed for production-type felling for cutting clean wood. This is the fastest type of cutter in clean wood; however, it dulls the fastest in dirty or fire-hardened wood and requires special training to sharpen.
  Semi-chisel: A less aggressive cutter type than a chisel cutter. A round file is used when filing a semi-chisel chain. The semi-chisel cutter is more tolerant of dirt and dust and stays sharp longer than the other cutters.
Explain there are also low-kickback chains available with chipper, chisel, and semi-chisel cutters. These are used for training inexperienced sawyers. The chain cuts smoothly and is ideal for cutting brush, small-diameter material, dimensional lumber, house logs, and other materials that aren’t usually cut with chainsaws. Less aggressive cutting angles and features added to the depth gauge and drive links provide a lower kickback response.

## Slide 6: Safety Check Video
Notes: Remind students that it is essential to conduct a chain saw safety check before starting operations.
Play the video about performing a safety check.
After the video finishes, ask students to describe how to perform a safety check. Responses should include:
  Chain brake: Confirm the chain brake locks and unlocks properly.
  Throttle trigger and interlock: ensure the throttle trigger cannot be squeezed without first depressing the throttle interlock on the top of the handle. This keeps the throttle from being activated by sticks or branches when you are not holding the rear handle.
  Chain catch: Confirm the chain catcher is present.
  Anti-vibration system: Check that the anti-vibration system and fasteners are tight by turning the chainsaw upside down and confirming nothing is loose.
  Spark arrester screen: check that the spark arrester screen is present.
Ask students if there are any questions.

## Slide 7: Avoiding Fuel Geysers
Notes: Ask students to share what they think a fuel geyser is.
After students have a chance to respond, tell them you will play the video describing a fuel geyser.
After playing the video, tell students that when refueling their chainsaws in the field, they need to be careful to avoid fuel geysers.
Explain that a fuel geyser is the forceful expulsion of liquid and vapor fuel from the fuel tank caused by the rapid depressurization of the tank. Heat and agitation cause the pressure in the tank to increase. A delayed fuel geyser can occur after opening the fuel container.
Tell students that fuel geysers can occur any time fuel, heat, and pressure are combined in fuel transport containers or small, gas-powered engines, such as chainsaws, leaf blowers, and portable pumps. Fuel geysers can result in injury when fuel is sprayed and comes in contact with an operator’s skin and eyes.
Tell students to take the following precautions and mitigations when fuel, heat, and pressure are present or suspected:
  Always assume fuel tanks and fuel containers are pressurized. Shut the saw off to allow it to cool. Restart the equipment when it is cool.
  Always check fuel levels before opening the fuel tank or filler cap. Fuel levels greater than half a tank are more likely to geyser.
  Always move away from the fireline or any ignition source. This includes moving at least 20 feet or more from any heat source and 10 feet from the fueling area.
  Cover the fuel cap with a rag when opening to contain potential fuel geyser spray. While maintaining downward pressure on the cap, slightly open it to allow excess pressure to escape and listen for the sound of gas releasing. Once the pressure subsides, continue fully opening the cap.
  Be extra vigilant when equipment is running poorly, and the fuel level is above half a tank. If you notice that the tank is bubbling, this is an indicator of the potential for future fuel geysering and vapor lock.
    Vapor lock refers to how the vaporization of gas in the fuel tank and fuel lines build pressure so that the tank is deprived of fuel. The chainsaw may not start or may get bogged down despite having a full gas tank.
  Do not use fuel older than one month; winter fuel is believed to be a contributing factor.
If time allows, review an incident from the Lessons Learned Center about fuel geysering.

## Slide 8: Personal Protective Equipment
What types of personal protective equipment (PPE) should you wear for chainsaw operations?
Notes: Ask students to answer the following question: “What types of personal protective equipment (PPE) should you wear for chainsaw operations?”
As students respond, take notes on flip chart paper or a whiteboard.
Make sure that the following items are covered:
  Chaps
  Gloves
  Helmet
  Eye/Face protection
  Boots
  Hearing protection
  Long pants and long sleeve shirt for unit exercises
Note that this is the same set of PPE as for when using chainsaws generally. The only difference is that the PPE for fire use is made of Nomex, a fire-retardant fabric.
Tell students to check to make sure their equipment is in good working order. For example, they should ensure their PPE doesn’t have holes and that the chain on their chainsaw is sharp.

## Slide 9: Overview of Activities
Students will participate in activities where they need to:
  Wear proper PPE.
  Identify chainsaw components.
  Perform chainsaw maintenance.
  Perform a chainsaw safety check.
  Start and stop a chainsaw.
Notes: Tell students that they will now go outside (or to a designated area) to practice the following tasks:
  Wearing proper PPE.
  Identifying chainsaw components.
  Performing chainsaw maintenance.
  Performing a chainsaw safety check.
  Starting and stopping a chainsaw.
Tell students they will work in small groups with a coach for each activity.
Tell students that their assigned coach will provide a demonstration before they perform each task.
Instruct students to use the IRPG and NWCG Standards for Wildland Fire Chainsaw Operations, PMS 212, as resources for completing the activities.
Ask students if there are any questions before you head outside.
Tell students to meet with their assigned coach at a pre-identified location.

## Slide 10: Conclusion Slide
Notes: Close with the following summary points:
  Always wear the appropriate PPE and check that it is in working order before starting and operating the chainsaw.
  Always complete the safety check before operating the chainsaw, and keep your chainsaw and other tools maintained.
  Keep both hands on the saw and make sure you are well-balanced when operating a chainsaw.
Ask students if they have any questions.