## Slide 2: Unit 3 Objectives
Define the duties and responsibilities of the chain saw operator and the swamper.
Explain the tactical application of chain saws in fireline construction and mop up operations.
Describe methods of saw team deployment for fireline tactical strategy.
Describe methods for mop up and fireline rehabilitation.

## Slide 3: Line Construction Video
Please click video window to play media.

## Slide 4: Duties and Responsibilities of the Saw Team

## Slide 5: Chain Saw Operator
Monitors fire:
    Establishes communication
    Ensures LCES are in place

## Slide 6: Chain Saw Operator
Establishes cutting area control.

## Slide 7: Chain Saw Operator
Applies appropriate line construction standards for fireline width, limbing height, safety zones, and MIST
Adjusts line construction standards based on fuel type and fire behavior
Makes line location decision when location has not been flagged by a line scout

## Slide 8: Chain Saw Operator
Sets team’s work pace
Cuts moveable pieces
Safely moves between cutting locations

## Slide 9: Chain Saw Operator
Creates disposal sites for cut material like keyholes or windows
Fells hazard trees if qualified to do so
Bucks burning material during mop up

## Slide 10: Swamper
Assists with cutting area control and establishing fireline:
  Maintains LCES
  Acts as communication link for saw team
  Clears fireline as an escape route
  Improves safety zones
Notes: Messed up bullets again

## Slide 11: Swamper
  Dragging
  Chaining
  Banking
  Throwing
Moves cut material along the fireline by:

## Slide 12: Sawyer and Swamper Video
Please click video window to play media

## Slide 13
Keyholes
Slide-3-13
Slide 3-13
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S

## Slide 14
Slide-3-14
Slide 3-14
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 15
Slide-3-15
Slide 3-15
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 16
Slide-3-16
Slide 3-16
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 17
Slide-3-17
Slide 3-17
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 18
Slide-3-18
Slide 3-18
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 19
Slide-3-19
Slide 3-19
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Keyholes

## Slide 20
Please click video window to play media.
Keyhole Video

## Slide 21: Banking

## Slide 22
Slide-3-22
Slide 3-22
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Banking

## Slide 23
Slide-3-23
Slide 3-23
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Banking

## Slide 24
Slide-3-24
Slide 3-24
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Banking

## Slide 25
Slide-3-25
Slide 3-25
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Banking

## Slide 26
Slide-3-26
Slide 3-26
Unit 3 – Fireline Construction and Mop Up
S-212
W I L D L A N D F I R E C H A I N S A W S
Banking

## Slide 27: What would be an example of saw team deployment in your area? Example: Pull two-person teams off local engines vs. having a crew with dedicated sawyers.

## Slide 28: Topographic Considerations
Terrain will often dictate line location, cutting area control, escape routes, and safety zones:
  Make sure workers below the cutting area are warned and clear of bucking and felling operations.
  Apply the Downhill/ Indirect Line Construction Guidelines.
Slide-3-28

## Slide 29: Tactical Considerations
Avoid unnecessary felling.
Remove hazardous or hangup trees up to your skill level or flag them.
No felling should occur when top and lay cannot be observed.
Pay attention to fire behavior while locating and constructing fireline.

## Slide 30: Tactical Considerations Fire-Weakened Trees

## Slide 31: Tactical Considerations-Fire-Weakened Trees

## Slide 32: Employ MIST
Flush-cut stumps.
Locate fireline away from larger fuels.
In wilderness areas, avoid all tree felling and bucking if possible.

## Slide 33: Tactical Deployment
Slide-3-33

## Slide 34: Direct Attack
Remove larger fuels and brush.
Swampers watch for spotting.

## Slide 35: Indirect Attack
May require multiple saw teams, crews, and mechanized equipment.

## Slide 36: Initial-Attack Tactics
Sawyer and swamper should each carry a hand tool.
If creating saw teams from different engines, ensure a good swamper briefing is done.

## Slide 37
Each saw team cuts a swath of fireline, with the lead team only cutting enough fuel to pioneer the fireline, and the following saw teams completing the fireline with hand tools.
Slide-3-37
Progressive Line Construction

## Slide 38
Slide-3-38
Progressive

## Slide 39
Slide-3-39
Progressive

## Slide 40
Slide-3-40
Progressive

## Slide 41
Slide-3-41
Progressive

## Slide 42
Slide-3-42
Progressive

## Slide 43
Slide-3-43
Progressive

## Slide 44
Slide-3-44
Progressive

## Slide 45
Slide-3-45
Progressive

## Slide 46
Please click video window to play media.
Progressive Video

## Slide 47: Leap Frog Line Construction
The saw team cuts a chain of fuel and then bumps a chain ahead, followed by hand crews to complete the fireline. Works well in light fuels or during mop up.

## Slide 48
Leap Frog
Slide-3-48

## Slide 49
Slide-3-49
Leap Frog

## Slide 50
Slide-3-50
Leap Frog

## Slide 51
Slide-3-51
Leap Frog

## Slide 52
Slide-3-52
Leap Frog

## Slide 53
Slide-3-53
Leap Frog

## Slide 54
Slide-3-54
Leap Frog

## Slide 55
Slide-3-55
Leap Frog

## Slide 56
Please click video window to play media.
Leap Frog Video

## Slide 57: Mop Up
Mitigate hazards.
Facilitate crew access.
“Sport” felling is forbidden!
Maintain LCES during mop up.

## Slide 58: Fireline Rehabilitation
Sawyers support crews by cutting material to rehabilitate fireline.
Provide cut material to stabilize fireline soils and direct runoff.
Wilderness areas require less impacting rehab techniques, such as:
  Flush-cutting stumps and staubs
  Employing MIST to minimize site disturbance

## Slide 59: Review Unit 3 Objectives
Define the duties and responsibilities of the chain saw operator and the swamper.
Explain the tactical application of chain saws in fireline construction and mop up operations.
Describe methods of saw team deployment for fireline tactical strategy.
Describe methods for mop up and fireline rehabilitation.